## Slide 1
Urban and Regional Models: Integration across Space, Time and Policy Fields
Michael Wegener
Symposium Integration of Land-Use and Transport Models
TUM Science & Study Center, Raitenhaslach, 2-4/11/2016

## Slide 2
Objective
2

## Slide 3
Objective
Most urban and regional models have been developed for different policy fields at different levels of spatial and temporal resolution.
But it has become apparent that urban policy fields are interdependent and need to be modelled together.
The first urban and regional models were aggregate in space and static in time. More recently new data sources and computer techniques have stimulated a trend towards ever more disaggregation in space and time.
This paper argues for models that are instead multi-level and multi-scale in subsystems, space and time.

## Slide 4
Trends in Urban Modelling
4

## Slide 5
CAL
SAL
TOP
IRP
MEP
Urban models in the 1980s
OSA
LIL
HUD
POL
BOY
ITL
KIM
5
Urban models today
5
RUR
CUF
ILU
IMR
TRE
KIM
MUS
POL
TRA
ITL
URB
TLU
MET
DEL
MEP
ILM
PEC
MAR
STA
IRP
PUM
TXL

## Slide 6
Trends in urban modelling
Development path
(adapted from Miller et al. 1998)
MEP
CUF
KIM
POL
STA
ILT
MAR
DEL
IRP
MET
IMR
MPL
MUS
RUR
PEC
TRA
TRE
TLU
TXL
ILM
URB
PUM

## Slide 7
ILUMASS
7

## Slide 8
The ILUMASS project (2001-2006)
The project ILUMASS (Integrated Land-Use Modelling and Transport Systems Simulation) combined
a microscopic activity-based simulation model of urban traffic flows
a microscopic agent-based model of household and firm development and the resulting changes of land and housing markets.
a model of environmental impacts.

## Slide 9
ILUMASS
model
Firms
- floorspace
- firms
- jobs
Person travel
demand
- activities
- week plans
- trips
Goods trans-port demand
- activities
- trips
Environmental impacts
Emissions
- air pollution,
- traffic noise
at sources
Population
- housing
- households
- persons
- cars
Dynamic
assignment
- link flows
Impacts
- air quality,
- traffic noise
at work
Impacts
- air quality
- traffic noise
at housing
Accessibility
- of jobs
- of shops
- of population
- of facilities
Land use
Transport

## Slide 10
ILUMASS model dimensions
1.2 million households
2.6 million persons
1.2 million dwellings
80,000 firms
92,000 industrial sites
8,400 public transport links
848 public transport lines
13,000 road links
246/54 internal/external zones
209,000 raster cells
30 simulation periods (years)
3-5 days computing time)
Conclusions

## Slide 11
Firms
Firms/households
11
New firms
New households
Firms/households
11
New firms
New households
Firms/households
11
New firms
New households
Firms
Firms/households
11
New firms
New households
Births(Deaths ►

## Slide 12
Households
Births/deaths
12
Births
Deaths
Households
Births/deaths
12
Births
Deaths
Households
Births/deaths
12
Births
Deaths
Households
Births/deaths
12
Births
Deaths
Households
Births/deaths
12
Births
Deaths
Households
Births/deaths
12
Births
Deaths
Dwellings ►

## Slide 13
Households
Dwellings
13
New dwellings
Demolitions
13
New dwellings
Dwellings
13
Households
Dwellings
13
New dwellings
Demolitions
Households
Dwellings
13
New dwellings
Demolitions
Moves ►

## Slide 14
Households
Moves
14
Outmigration
Immigration
New household
Move
14
Outmigration
Immigration
New household
Move
Moves
Moves
14
Outmigration
Immigration
New household
Move
Moves
14
Outmigration
Immigration
New household
Move
Moves
14
Outmigration
Immigration
New household
Move
End of ILUMASS ►

## Slide 15
The end of ILUMASS
The ILUMASS project was quite successful.in developing individual submodels..
However, it was not successful in implementing the planned integrated model of land use and transport:
The land use, transport and environment submodels of ILUMASS were independent executables.
The application programming interface (API) connecting submodels via files never worked properly.
Data exchange between submodels was slow.
The computing times of the transport submodels took days for each year.
Conclusions

## Slide 16
The "little" ILUMASS
After the end of the project the Dortmund group decided to replace the microscopic transport and environmental sub-models were replaced by the aggregate transport model of the IRPUD model and by simpler environmental impact models.
The resulting "little" ILUMASS model consisted of only two executables and took only 90 minutes for the whole 30-year simulation.
Conclusions

## Slide 17
Mircosimulation
17

## Slide 18
Microsimulation
New activity-based microsimulation models improve
urban simulation models:
- Lifestyles can be represented, i.e. households and individuals can be disaggregated to the agent level.
- Environmental impacts and feedback can be modelled with the required spatial resolution.
- Population and employment can be represented by their decision making units, i.e. households and firms.
- Microlocations can be represented. Households affected by environmental impacts can be localised.
PROPOLIS & ILUMASS

## Slide 19
However ...
To date, no full-scale microsimulation model of urban land use, transport and environment has become operational.
There are still unresolved problems regarding the inter-faces between the submodels.
The feedback between transport and environmental quality and location has not yet been implemented.
The computing time for existing models is calculated in terms of weeks or days, not hours.
Serious problems of calibration, instability and random fluctuations have not yet been solved.
Conclusions

## Slide 20
Stochastic variation
1000 choices
100 alternatives
Wegener (2011)
20
Stochastic variation
20
1000 choices
400 alternatives
Wegener (2011)
Stochastic variation
20
1000 choices
900 alternatives
Wegener (2011)

## Slide 21
Limits of microsimulation
There are ultimate limits to increasing the substantive,
spatial and temporal resolution of behavioural models:
- There are theoretical limits when the number of pro-cesses simulated is too small to yield reliable results.
- There are empirical limits when the marginal costs of obtaining micro data are larger than their added value.
- There are practical limits when the computing time of the models exceed the duration of the modelled processes.
- There are ethical limits to the collection of data about private lives for purposes of research.
Conclusions

## Slide 22
How much micro is enough?
There seems to be little consideration of the benefits and costs of microsimulation:
- Where is microsimulation really needed?
- What is the price for microsimulation?
- Would a more aggregate model do?
For spatial planning models, the answer to these questions depends on the planning task at hand.
Conclusions

## Slide 23
Multi-level, Multi-scale Models
23

## Slide 24
Model levels
Dortmund
Regions
Dortmund
Zones
Dortmund City
Raster cells
Multi-level
Multi-scale

## Slide 25
Level 1: regions
Dortmund
Regions
Dortmund
Zones
Dortmund City
Raster cells

## Slide 26
SASI model
GDP
Accessibility
Production
function
Employment
Migration
function
Population
Income
Labour
force
Transport
policy
Unemploy-
ment

## Slide 27
Scenario A1
GDP per capita
Difference from
Scenario A-1
in year 2031
8 - 10
6 - 8
4 - 6
2 - 4
0 - 2
-2 - 0
-4 - -2
-6 - -4
-8 - -6
-10 - -8
Dortmund
27
Scenario B1
GDP per capita
Difference from
Scenario A-1
in year 2031
8 - 10
6 - 8
4 - 6
2 - 4
0 - 2
-2 - 0
-4 - -2
-6 - -4
-8 - -6
-10 - -8
Dortmund
27
Scenario C1
GDP per capita
Difference from
Scenario A-1
in year 2031
8 - 10
6 - 8
4 - 6
2 - 4
0 - 2
-2 - 0
-4 - -2
-6 - -4
-8 - -6
-10 - -8
Dortmund
27

## Slide 28
Level 2: zones
Dortmund
Regions
Dortmund
Zones
Dortmund City
Raster cells

## Slide 29
IRPUD model
Population
households
Nonresidential
buildings
Residential
buildings
Employment
Workplaces
Transport
market
Market for
nonresidential buildings
Land
market
Labour
market
Housing
market
Microsimulation
from SASI model

## Slide 30
30
CO2 emission by transport per capita per day (kg)
30
-20%
30
30
30
CO2 emission by transport per capita per day (kg)
30
-20%
30
CO2 emission by transport per capita per day (kg)
30
CO2 emission by transport per capita per day (kg)
30
-20%
30
CO2 emission by transport per capita per day (kg)
30
CO2 emission by transport per capita per day (kg)
-30%
30
30
30
CO2-Emissionen Verkehr je Einwohner je Tag (kg)
30
CO2-Emissionen je Einwohner je Tag (kg)
-20%
30
CO2-Emissionen Verkehr je Einwohner je Tag (kg)
30
CO2-Emissionen je Einwohner je Tag (kg)
-30%
30
CO2 emission by transport per capita per day (kg)
-40%
30

## Slide 31
Level 3: raster cells
Dortmund
Regions
Dortmund
Zones
Dortmund City
Raster cells

## Slide 32
Environmental and social impacts
Impacts
- Resource use
Input
Spatial disaggregation
GIS database
- Zones
- Networks
- Land use
IRPUD model output
- Population by zone
- Employment by zone
- Floorspace by zone
- Traffic by link
Raster data
- Cars
- Trains
- Busses
- Speeds
Raster data
- Population
- Employment
- Floorspace
- Traffic
Impacts
- Traffic noise
Impacts
- Emissions
Impacts
- Environment
Impacts
- Air quality
Impacts
- Accessibility
Raster model

## Slide 33
Raster model
Air quality
33
Raster model
Traffic noise
33

## Slide 34
New Challenges
34

## Slide 35
New challenges for urban models (1)
To cope with the new challenges of energy scarcity and
climate change urban models need to be able to predict
the decision behaviour of households and firms under
fundamentally different conditions:
Climate change: mitigation
- high carbon or fuel taxes
- high road pricing or congestion charges
- heavy use of public transport
- rigorous speed limits, car-free zones
Climate change: adaptation
- flood prevention and management
- rigorous land use controls to prevent development
in floodplains and fresh-air corridors
(continued)

## Slide 36
New challenges for urban models (2)
Energy scarcity:
- alternative vehicles/fuels
- decentralised energy (solar, geothermal, photovoltaic)
- heat insulation of buildings
Social conflicts:
- groups/communities most affected by climate change
and energy scarcity
- minimum standards of access to basic services
New technologies:
- car-sharing
- online shopping
- self-driving cars

## Slide 37
The Ruhr Model
37

## Slide 38
Polycentric Ruhr Area
38

## Slide 39
Ruhr model networks
39

## Slide 40
Ruhr model internal zones
40

## Slide 41
Ruhr model raster cells
70 km
120 km
41

## Slide 42
Ruhr model
Population
households
Nonresidential
buildings
Residential
buildings
Employment
Workplaces
Transport
market
Market for
nonresidential buildings
Land
market
Labour
market
Housing
market
Microsimulation
Energy
CO2
Energy
CO2
Energy
CO2
Energy
CO2
Energy
CO2

## Slide 43
Energy-retrofitted residential buildings 2050 (%)
Scenario A31
43

## Slide 44
Scenario A33
Station-less car-sharing cars 2050 (%)
44

## Slide 45
Comparison of scenarios

## Slide 46
Comparison of scenarios

## Slide 47
Conclusions
47

## Slide 48
Urban models and fundamental change
The fundamental changes in the problems and priorities
of urban planning will have deep impacts on the philoso-phy and method of urban modelling:
- less detail, more basic essentials
- less extrapolation, more fundamental change
- less equilibrium, more dynamics
- less observed behaviour, more theory on needs
- less preferences and choices, more constraints
- less calibration, more plausibility analysis
- less forecasting, more backcasting (don't ask what
can be done but what needs to be done)

## Slide 49
Multi-level, multi-scale models
These considerations lead to a reassessment of the hypo-thesis that in the future all spatial modelling will be micro-scopic and agent-based.
Under constraints of data collection and of computing time, there is for each planning problem an optimum level of conceptual, spatial and temporal resolution.
This suggests to work towards a theory of balanced multi-level models which are as complex as necessary for the planning task at hand and – to quote Albert Einstein – "as simple as possible but no simpler".
Conclusions

## Slide 50
More information
Wagner, P., Wegener, M. (2007): Urban land use, transport and environment models: experiences with an integrated microscopic approach. disP 170 (3/2007), 45-56. http://www. spiekermann-wegener.de/pub/pdf/PWMW_ILUMASS.pdf
Wegener, M. (2011): From macro to micro – how much micro is too much? Transport Reviews 31, 2, 161-177.
ILUMASS model:
http://www.spiekermann-wegener.de/mod/ilumassmod.htm
STEPs project:
http://www.spiekermann-wegener.de/pro/steps.htm
Ruhr model:
http://www.energiewende-ruhr.de/
http://www.spiekermann-wegener.de/pro/ruhr2050.htm